## Slide 1: Integration of Environment Manipulation within the Navigation Topology:
Bachelor End Project – 05/07/2022
Ismail Elmasry, Bachelor Candidate
Department of Mechanical Engineering, Control Systems Technology group, Tech-united@home

## Slide 2: Outline:
Current Navigation Stack Architecture
Problem Formulation
Assumptions and Simplification
Performance Measures
Conceptualization
Implementation
Experimental setup & Results
Future work
Conclusion

## Slide 3: Current TU/e Navigation Stack For Hero
A Hierarchical motion planning system which consists of:
    Global Planner: provides connectivity information to the global goal with the use of an A* search algorithm.
    Local planner: The steering commands are made using DWA
    Executive : A general state machine which provides goals to the motion planner. The recovery behavior is also implemented in this module as it knows more information about the world and the task being executed.

## Slide 4
Problem Formulation

## Slide 5: Problem Formulation (Door opened)
Notes: NAMO problem; NP-hard for simple case
computational complexity theory, NP-hardness is the defining property of a class of problems that are informally "at least as hard as the hardest problems in NP"

## Slide 6: Problem Formulation (Door closed)

## Slide 7: Problem Definition
Design and implement a planner which combines motion planning and object manipulation, using geometric and symbolic information from the world model to allow navigation among movable objects in domestic environments.

## Slide 8: Assumptions and Simplifications:
Robot can manipulate Known objects by pushing at set contact points.
Robot is the only autonomous entity in the environment.
Robot can detect dynamic obstacles.
The dynamic obstacles are placed in the environment in such a way to ensure linearity of the problem.

## Slide 9: Problem Linearity
A problem is Linear if there exists a sequence of independent objects that could be moved to connect two disjoint components of the free configuration space.(no cascading effect)
Figure: Sequence of objects blocking path (Stilman et al.[2004]):

## Slide 10: Performance Measures
1. Generates the path with the shortest distance.
2. Uses the least amount of work.
3. Can adapt to different blocking locations along the path.
4. Can adapt to different object dimensions and orientations blocking the path.
5. Can differentiate between static and dynamic obstacles.

## Slide 11
Conceptualization

## Slide 12: Conceptualization -1- Set Point Definition

## Slide 13: Conceptualization -2- Configuration Space Partitioning

## Slide 14: Conceptualization -3- Global & Local Map Seperation

## Slide 15: Stilman et al. [2004] Approach:
    Utilizes the concept of connecting disjoint configuration spaces.
    Applies grasping and pushing manipulations based on predefined setpoints.
WU & Levihn [2010] Approach:
    Utilizes the concept of Map separation to find objects blocking path.
    Applies manipulation by dividing navigation path into 3 sub edges.
Notes: n algorithm intended to locate a local optima. It is suited to traversing a given region of the search space and getting close to (or finding exactly) the extrema of the function in that region.
If a path exists, it finds it in finite time. – If a path does not exist, it returns in finite time. Start. Goal.

## Slide 16
Implementation

## Slide 17: Pseudocode Implementation:

## Slide 18: Pseudocode Implementation:
    Enumerate():
        Where is the dynamic object?
    PLAN_OBJECT():
      Which object to manipulate?
    MANIP_OBJECT():
      How to manipulate and is it removed?

## Slide 19
Experimental Setup & Results

## Slide 20: Experimental Setup:
- The grid map generated from PNG
The grid maps are 425x425 pixels with a cell size of 1.
- The occupancy threshold value is 0.49.
- Boundary walls were given the occupancy value of 0.92 (threshold.Ostatic).
- Dynamic objects were given the occupancy range from 0.8 to 0.92 (excluding).
-Static objects were given an occupancy value below 0.8 (threshold.Oboundary).
-The initial pose () is indicated as a red dot.
- The Goal pose ()is indicated as a green dot

## Slide 21: Scenario -1- No constraining object
Goal pose 1: (360,330)
Goal pose 2: (210,240)
Goal pose 3: (50,50)

## Slide 22: Scenario -2- Constraining Object not blocking path
Goal pose 1: (100,400)
Goal pose 2: (50,50)
Goal pose 3: (360,330)

## Slide 23: Scenario -3- Constraining Object Blocking Path
a) Dynamic object detected
b) Navigated to dynamic object and attempting manip.
c) Navigation to goal pose

## Slide 24: Scenario -4- Constraining Object at different location
a) Dynamic object detected
b) Navigated to dynamic object and attempting manip.
c) Navigation to goal pose

## Slide 25: Scenario -5- Static Constraining Object
a) Static object blocking path
b) Return message

## Slide 26
Future Work

## Slide 27: Future Work and Extensions
Object placement planning
Object Manipulation
More than one dynamic obstacle classification.
Updating the Navigation Stack architecture for real life testing
Figure: Updated the Navigation stack architecture

## Slide 28: Conclusion:
Generates the path with the shortest distance.
Uses the least amount of work.
Can adapt to different blocking locations along the path.
Can adapt to different object dimensions and orientations blocking the path.
Can differentiate between static and dynamic obstacles.
Locally optimal

## Slide 29: Thank you!